## Slide 1: Out of Region Market Assumption
Resource Adequacy Technical Committee
December 1, 2011

## Slide 2: Steering Committee Recommendations
Oct 4th Steering Committee recommended that the Out of Region Market Assumption Analysis should examine:
  Making the CPUC load forecast look forward
  The impact of Once-Through-Cooling (OTC) retirements in California on available SW supply

## Slide 3: California CPUC load forecast
The CPUC load forecast looks backward – latest assessment is the 2010 load forecast
The RA Standard looks forward – 3 to 5 years out
Used historical CPUC assessments (2006 to 2010) to develop trend lines for both winter and summer load forecasts

## Slide 4: Winter Trend Lines

## Slide 5: Summer Trend Lines

## Slide 6: Load Forecast Conclusions
Propose no increase in winter load forecast
Summer peak loads are increasing; however
  Assuming 0 import capability in the summer anyway
  If California resource adequacy metric assumes that it will plan to meet the summer peak plus a 15% planning margin – this should leave additional winter capacity for import

## Slide 7: OTC – Clean Water Act
The 1972 Clean Water Act – section 316(b) requires that the location, design, construction and capacity of cooling water intakes reflect best technology available
In May 2010, the California Water Resources Board (Board) adopted a statewide water quality control policy on the use of Once-Through-Cooling (OTC) to implement section 316(b)
The policy outlines a phased implementation schedule which mandates compliance for OTC on or before certain dates
Closure dates in the table (page 9) are either from the owner (early closure) or from the Board

## Slide 8: OTC Retirements
All plants on this list are gas steam plants with an average on-line date of 1962
Not cost effective to retrofit these facilities with cooling systems
Some sites are being retrofitted with new combined cycle units – counted as new facilities not rerates
List does not include LADWP facilities or Diablo and Songs (Need to correct problems by 2022 and 2024 or face retirement)

## Slide 10: Proposed OTC Adjustment to Analysis:

## Slide 11: Gas-Fired Plants Under Construction
The CPUC RA assessment does not include these plants in their analysis

## Slide 12: Modified RA Assessment + Transfer Capability 2015 Analysis

## Slide 14: Conclusion:
In 2015, there is enough surplus in the state of California and enough transfer capability to support 3,000 MW of imports October to April
From May to September, California relies heavily on imports to support their resource adequacy efforts and therefore no import capability should be assumed
Same conclusions for October 4th, steering committee for the 2015 analysis

## Slide 15: Appendix - Power Plant Development in California
During the past 11 years there as been substantial resource development within the state of California – most of it gas-fired
Chart (page 10) includes all resources built in state regardless of owner
Chart (page 10) does not include 4,011 MW from table on page 5
Chart (page 7) “net addition” include the impact of plant retirements in the state (but also including Mohave)

## Slide 16
Source: Ventyx

## Slide 17
Net Additions = cumulative additions – cumulative retirements
California Cumulative and Net Resource Additions