## Slide 1: PNW Regional Contingency Resources
Resource Adequacy Technical Committee
April 6th, 2011

## Slide 2: Resource Adequacy Standard
2008 RA standard counts significant events: 28,800 MWhrs of energy (per season) or 3,000 MW of capacity (any 1 hour)
Any games that exceed these thresholds are considered a ‘miss’
Proposed alternative: build a contingency resource stack and count all misses
Assign contingency resources to various ‘buckets’ (by cost, control, stress, etc.) and evaluate use in Genesys post processing
First bucket (CR 1) – utility programs
Second bucket (CR 2) – non-utility emergency generators
Additional buckets?

## Slide 3: Utility Contingency Resources – CR 1
Includes Demand Response (DR) programs sponsored by load serving entities – direct control over loads and or resources either in real-time or day ahead
Most successful DR programs are for irrigation and A/C – good for peak shaving of summer peaking utilities
Other programs such as AGC standby generation can provide capacity and energy across seasons
Therefore it is necessary to track contingency resources by seasons and contributions to both energy and capacity

## Slide 4: PacifiCorp

## Slide 5: Idaho Power and PGE

## Slide 6: Summary of CR 1

## Slide 7: CR 2 – Data Center Emergency Generation