## Slide 1: September 28, 2012 Draft Assessment Results
Technical Committee Meeting
September 28, 2012

## Slide 2: Other Assumptions
How many games do we need to do?
  There are 80 water years (sequential draw) , 77 load years (random draw), and wind year is lock-stepped with load year
  Random draws do not cover all unique combinations of water and load/wind unless we do a large number of games
  Too few games can produce uneven results
Which wind year set do we use?
  There are 20 sets of temperature-correlated wind capacity factors
Look at “instantaneous” LOLP

## Slide 5: Number of Games
How many games? … (80 x 77 = 6160)
  Sequential water pairs uniquely with load/wind by using a cycled sequence for the load years
  Game #1 pairs 1929 water with 1929 load, and the run is essentially in lockstep for the first 77 games (game #77 pairs 2005 water and load)
  Game #78 pairs 2006 water with 1929 load
  Water year 1929 pairs with load year 1929, 1932, 1935, … , and so on

## Slide 6: Wind Capacity Sets
Which one?
  For now, we selected set #18, which tested at the mid-range for LOLP at 4900 games
  The test cases were done using older assumptions (70-year hydro, some differences in wind totals, other resources)

## Slide 7: Wind Capacity Sets

## Slide 8: Draft Assessment Results

## Slide 9: Draft Assessment Results

## Slide 15: September 28, 2012 Assessment