## Slide 1: Avista’s Flexibility Overview
James Gall
Senior Power Supply Analyst
Contact:
James.gall@avistacorp.com
509.495.2189
1

## Slide 2: Overview
System & Resource Overview
Off system sales
Palouse Wind
IRP Planning
Future Studies
2

## Slide 3: Avista Balancing Authority
  2,764 megawatts, 54 turbines
  Two cascading hydro systems, 8 dams
  Multiple 3rd party sales and purchases contracts
Resource Mix (megawatts)

## Slide 4: Flexible Resource Overview
Hydro:
  Noxon Rapids: AGC, load following, contingency reserves
  Cabinet Gorge: load following, contingency reserves
  Long Lake: load following, contingency reserves
Thermal
  Coyote Springs 2: load following, AGC capable
  Colstrip: load following
  Northeast: supplemental reserves
  Rathdrum CT: supplemental reserves
Contracts
  Mid-Columbia: AGC, contingency reserves
4

## Slide 5: Dynamic Capacity Sales
First in nation market based rate authority for Ancillary Services Sales (Tariff 9)
Current Sales
    Provide Dynamic Capacity (imbalance services) to local PUD and aluminum rolling mill
      - 3rd Party Schedule hourly product, Avista serves within hour variation
    5 MW dynamic sale and spin reserves to neighboring control area
    Iberdrola imbalance market
    Past Sales
    Up to 21 MW up and 20 MW down for 41 MW range
    Up to 50 MW up and 50 MW down for 100 MW range

## Slide 6: Palouse Wind
Background
Developed by First Wind, owned by Palouse Wind LLC
30-year Purchase Power Agreement
Began Commercial Operation in December 13, 2012
105 MW (58- 1.8 Vestas V100 turbines)
Connected to Avista’s 230 kV Benewah-to-Shawnee Transmission Line
Expected capacity factor of 40 percent
Added to Avista’s portfolio to meet Washington State’s Energy Independence Act
Flexibility Implications
Contractual rights to curtail wind output with a cost
Limit ramp ups to 10 MW per minute
Typically hold 10 MW of capacity for wind following, during high winds hold 40 MW and depend on operating reserves for high speed cutouts

## Slide 7: Palouse Wind Output April 7th, 2013

## Slide 8: How Avista Met April 7th Palouse Wind Variation

## Slide 9: IRP Planning
Avista Wind Integration Study (2007)
2013 IRP Capacity Planning
  Long-term L&R balance accounts for operating reserves, regulation, and load and wind following needs
  Add integration costs for variable renewable options (wind/solar)
  Add integration benefits for certain resources (CTs, batteries, hydro)

## Slide 10: Future Studies
Avista is developing operations model to optimize generation for day ahead and real-time dispatch, the model will help traders with decision making.
  The model will suggest how to optimize generating units to hold reserves, set dispatch levels, make day ahead commitment decisions, and market transactions.
  Patent pending hydro algorithms are used to real-time dispatch hydro facilities based on unit level engineering level representation, including operating constraints.
The model can also be used for resource planning, such as wind/solar integration costs and valuation of flexible resources (battery/LMS100).