## Slide 1: IRP Review
IRPs with Significant Detail on Flexibility Assessment
  Portland General Electric
  Puget Sound Energy
Other IRPs

## Slide 2: Portland General Electric
Start with system dispatched to normal economic conditions
Wind curtailment not assumed for Decs
Demand curves based on load net wind at percentiles
Supply curves based on asset dispatch changes from starting state

## Slide 3: Puget Sound Energy
Production cost dispatch with AURORAxmp
Used load, wind, hourly scheduled interchange and forced outages for intra-hour flexibility simulation
95% confidence interval to assess hour-ahead need for balancing reserves
Proxy CPS2 score

## Slide 4: Other IRPs
Forecast reserve requirements
Wind integration studies
PacifiCorp forecast reserve supply
Qualitative evaluations, such as letter grade for flexible aspects of generators