## Slide 1: Stakeholder Workshop on Redeveloped GENESYS
RAAC/SAAC Technical Workshop
August 4th, 2021
John Fazio, Dan Hua and John Ollis

## Slide 2: Agenda Topics
Purpose of GENESYS Redevelopment
Review model setup, data structure and presentation to provide context
  Climate change inflows and temperature (load)
For the Columbia and major tributaries, compare the following for :
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range
Exploration of other Questions/Notes in the model:
  Hourly hydro flexibility
  Market interactions on thermal unit commitment
  Market and transmission utilization
  Role of reserves
Next steps list:
  What is in the queue to enhance/improve the modeling?
  What have we missed?

## Slide 3: Planned Timing for Each Day
9:00 am – 9:15 am: Introduction
9:15 am – 10:30 am: Work Session 1
10:30 am – 10:45 am: Break
10:45 am– 12:00 pm: Work Session 2
12:00 pm – 12:45 pm: Lunch
12:45 pm – 2:00 pm: Work Session 3
2:00 pm – 2:15 pm: Break
2:15 pm – 3:30 pm: Work Session 4

## Slide 4: Rules/Goals For the Work Sessions
These meetings are for stakeholders to ask questions to better understand the current state of the redeveloped GENESYS model and what is possible.
  We will be focused first on understanding the current state, and then
  On cataloguing next steps for improving the model in the near and long term.
We recognize different stakeholders have used GENESYS for a number of different reasons, which means that we value diverse feedback
  Council staff will use the redeveloped model as one of the main tools to understand adequacy and hydro operational issues
  Other stakeholders may still use the classic GENESYS or utilize information from this model to support their adequacy/planning work.

## Slide 5: Guiding Principles for Redevelopment
Post 7th plan it was clear risks on the power system were changing, what was needed to understand these risks?
  Policies and goals veering towards more clean and renewable grid.
  Adding resources that fulfilled those policies have different characteristics and risks associated than with traditional baseload resources and hydro
  Reexamine assumptions and simplifications in modeling to get the best answer we can.
https://www.nwcouncil.org/energy/energy-advisory-committees/system-analysis-advisory-committee/genesys-%E2%80%93-generation-evaluation-system-model
This Photo by Unknown Author is licensed under CC BY
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA-NC
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 6: Review: Goals of Redevelopment
Serve Needs of Multiple Users and Uses
Currently used by the Council, BPA and other regional stakeholders.
Used for annual regional adequacy assessments, regulated hydro flow studies, and analysis of change in revenue due to differing hydro operations.
Maintain all necessary current functionality.
Answer new questions that previous model could not answer.
Notes: Needs to be discussed out explicitly
1) Prevent leaving important functionality behind.
2) Challenging because different users use the model to support a variety of analytics.
Multiple Users – Currently used by the Council, BPA and other regional stakeholders.
Multiple Uses – Used for annual regional adequacy assessments, regulated hydro flow studies, and analysis of lost revenue due to hydro dispatch change.

## Slide 7: Review: Goals of Redevelopment
Improve Model Accuracy
Co-optimize energy and reserve requirements by cost.
Better reflect forecast error and market economic effects on regional portfolio dispatch.
Incorporate future value of resources with storage into scheduling.
Incorporate emergency resources into dispatch.
Move from aggregate hydro to plant specific hourly dispatch.
Notes: Cannot study adequacy without consideration of economics in our region.
Time-dependent nature of the hourly hydro capability – model cascading of multiple dams as part of the system dispatch
Interaction between assignment of reserves and system capacity – incorporate reserves into an optimized dispatch
Trade-off between decisions for economics and adequacy – improved market representation
Representation of limitations on operators in dispatching the system – add fuel accounting and forecast error

## Slide 8: Review: Goals of Redevelopment
Improve Model Usability
Currently, model inputs, execution and output processing all are via FORTRAN.
Potentially keep FORTRAN for execution of code and structure, but incorporate an easier input and output processing interface.
Notes: Model support is currently by FORTRAN experts.
Input and output data management is challenging.

## Slide 9: What Are Similarities between the Models
Perform hourly simulation of regional hydro and thermal resource generation under varying stochastic inputs:
  Temperature variation (load)
  Wind and solar generation
  Water supply
  Thermal forced outages.
Incorporate all appropriate constraints of the Columbia River Basin and west-side hydro projects to replicate reasonable system operation on a period, daily and hourly basis.
Notes: The dispatch of resources is actually accomplished using resource stacking instead of evaluating each resource against a set electricity market price.

## Slide 10: Comparison – Model Usability
Attribute | Classic GENESYS | Redeveloped GENESYS
Model Interface | Fortran code, text and executable files | Web based GUI
Data Input/Output | Text files and sub routines to extract data (input/output) | Excel/GUI (input) and image/text/spreadsheet (output)
Data Storage | Local server/workstation | Cloud and local storage possible
Data Processing | Local server/workstation | Cloud and local capabilities

## Slide 11: Comparison – Model Functionality
Attribute | Classic GENESYS | Redeveloped GENESYS
Hydro Resources | Modeled in aggregate hourly, modeled individually monthly | Modeled individually for all stages
Topology | Regional resources and demand in two nodes and external market supply is one node | Multiple market and regional nodes with loads, resources and seasonal transfer limits
Energy and Reserves | Balancing reserves on hydro system only. Contingency reserve check | Co-optimized dispatch of energy and all reserves
Forecast Error | No error other than Thermal FOR | Forecast error for load and renewable resources affects unit commitment and market position, and thermal FOR
Value of Hydro | Input by user. Hydro block pricing relative to operating costs of specific resources | Future value of hydro explicitly calculated
Fuel Accounting | Modeled in aggregate hourly per sustained peaking limits, modeled individually monthly | For hydro, battery and gas plants on an individual basis.
Emergency Resources | Modeled in aggregate | Modeled individually

## Slide 12: Ongoing Work
Stakeholder Conference and Beyond
Continue to vet and communicate validated weekly constraints to stakeholders
Continue to incorporate and validate hourly constraints on the river system.
Continue to vet hourly simulated river operations with BPA and other stakeholders to ensure reasonable river operation with planning level data.

## Slide 13: Learnings So Far
Maintaining consistency with HYDSIM and hourly operational modeling assumptions is a challenge
Simulating operations with planning level data can sometimes create a disconnect, but seems to be OK for adequacy purposes
Incorporating market fundamentals helps close a disconnect between day to day planning and adequacy studies, but raises more questions about risk
As with all modeling exercises, this will continue to require reexamination of simplifications and assumptions

## Slide 14: River Operations on the Columbia and Tributaries
Review data sources, assumptions and structure
Individual plant operations: generation, spill, reservoir elevations, total flow

## Slide 15: The Two Adequacy Models and Historical Data
Comparisons of hydro-project data between:
  Classic GENESYS vs Redeveloped GENESYS
  Classic GENESYS vs Historical data
  Redeveloped GENESYS vs Historical data
For each hydro-project upstream of Bonneville, compare the four types of data:
  Total Outflow - spilled and turbined flow
  Generation – generation from the plant
  Elevation – elevation of the forebay of the reservoir
  Spill – flow through or over the plant not used for power generation

## Slide 16: The Hydro Projects

## Slide 17: The Hydro-Projects
GENESYS model operations for the same 76 HDYSIM hydro-projects
Some of the major reservoirs are shown in map

## Slide 18: The 55 Projects Upstream of Bonneville
U.S. Projects
Canadian Projects

## Slide 19: The GENESYS 55 Hydro Projects (I)
(SKQ)
reservoir
run-of-river

## Slide 20: The GENESYS 55 Hydro Projects (II)
gauging station
from Thompson Falls

## Slide 21: The GENESYS 55 Hydro Projects (III)
from Chief Joseph
from Oxbow

## Slide 22: Running the Two Adequacy Models

## Slide 23: Modeling the Northwest Power System
The two adequacy models are run to simulate the Northwest power system for the year 2025

## Slide 24: Data for Two Models
Both the Classic and Redeveloped GENESYS models are run with climate data for the three climate scenarios:
  A: CanESM2_RCP85_BCSD_VIC_P1
  C: CCSM4_RCP85_BCSD_VIC_P1
  G: CNRM-CM5_RCP85_MACA_VIC_P3
  more details available in the River Management Joint Operating Committee (RMJOC) report: https://www.bpa.gov/p/Generation/Hydro/hydro/cc/RMJOC-II-Report-Part-I.pdf )
The models are run with the climate data (streamflow, temperature and wind) for 2020 – 2029 using one historical hourly wind-profile

## Slide 25: Classic GENESYS
BPA provided modified streamflows, flood control rule curves and constraints for the 3 climate scenarios to run the HYDSIM hydro-regulation model in classic GENESYS
HYDSIM output contains 14 end-of-period (Oct, Nov, …, Apr_1, Apr_2, …, Aug_1, Aug_2, Sep) storages for the reservoir projects
These HYDSIM regulations for the projects satisfy all the input constraints according to a priority list

## Slide 26: Redeveloped GENESYS (I)
These 14 end-of-period HYDSIM storages are interpolated into weekly time-steps to regulate the GENESYS weekly reservoir storages
For the weekly time-steps, the GENESYS reservoir regulations should also satisfy the same constraints as HYDSIM
However, there are also some deviations from following HYDSIM

## Slide 27: GENESYS (II)
U.S. Projects
Canadian Projects
HYDSIM run-of-river projects become Redeveloped GENESYS reservoirs
Redeveloped GENESYS has different regulations for these reservoirs

## Slide 28: Properties of the 3 Selected Climate Scenarios

## Slide 29: Climate Scenarios vs Historical Data
From the RMJOC report:
  Temperatures have already warmed about 1.5°F in the region since the 1970s.
  They are expected to warm another 1 to 4°F by the 2030s (2020 to 2049).
  Future precipitation trends are more uncertain, but a general upward trend is likely for the rest of the 21st century, particularly in the winter months.
  Already dry summer months could become drier.
  By the 2030s higher average fall and winter flows, earlier peak spring runoff, and longer periods of low summer flows are very likely.

## Slide 30: The Box-and-Whiskers Plot

## Slide 31: Historical and Climate Scenario A Regional Temperatures

## Slide 32: Historical and Climate Scenario C Regional Temperatures

## Slide 33: Historical and Climate Scenario G Regional Temperatures

## Slide 34: Historical and Climate Scenario A Modified Flows at the Dalles

## Slide 35: Historical and Climate Scenario C Modified Flows at the Dalles

## Slide 36: Historical and Climate Scenario G Modified Flows at the Dalles

## Slide 37: The Historical Data

## Slide 38: Historical Hydro Project Data Sources
The Corps of Engineers website
  https://www.nwd-wc.usace.army.mil/dd/common/dataquery/www/
  Data for 25 U.S. projects (upstream of Bonneville) available
  Recent 10 years 2010 to 2019*
  Mostly hourly data, with some daily data
  All 4 types of data are mostly available
The Canadian Historical Hydrometric Data website
  https://wateroffice.ec.gc.ca/search/historical_e.html
  Data for 4 Canadian projects (upstream of Bonneville) available
  Recent 10 years 2009 to 2018
    Only daily data, and only 1 or 2 types of data available

## Slide 39: Comparisons between GENESYS and Historical Data

## Slide 40: Comparing Data (I)
GENESYS output are for 10 years of simulated hourly data using climate data
Historical data include 10 years of hourly and daily data
Comparisons of GENESYS with historical data are in terms envelopes and averages
  For hourly Data: as example, for Oct 1, 0th hour
    upper envelope for GENESYS data x is calculated by
      max( x10/1/2020 00:00:00, x10/1/2021 00:00:00, …, x10/1/2029 00:00:00 )
    lower envelope for GENESYS data x is calculated by
      min( x10/1/2020 00:00:00, x10/1/2021 00:00:00, …, x10/1/2029 00:00:00 )
      average for GENESYS data x is calculated by
      average( x10/1/2020 00:00:00, x10/1/2021 00:00:00, …, x10/1/2029 00:00:00 )

## Slide 41: Comparing Data (II)
  For daily Data: as example, for Oct 1
    upper envelope for GENESYS data x is calculated by
      max( x10/1/2020 00:00:00, x10/1/2020 01:00:00, …, x10/1/2020 23:00:00,
      x10/1/2021 00:00:00, x10/1/2021 01:00:00, …, x10/1/2021 23:00:00,
      …,
      x10/1/2029 00:00:00, x10/1/2029 01:00:00, …, x10/1/2029 23:00:00 )
    lower envelope for GENESYS data x is calculated by
      min( x10/1/2020 00:00:00, x10/1/2020 01:00:00, …, x10/1/2020 23:00:00,
      x10/1/2021 00:00:00, x10/1/2021 01:00:00, …, x10/1/2021 23:00:00,
      …,
      x10/1/2029 00:00:00, x10/1/2029 01:00:00, …, x10/1/2029 23:00:00 )

## Slide 42: Comparing Data (III)
  For daily Data: as example, for Oct 1
    average for GENESYS data x is calculated by
      average( x10/1/2020 00:00:00, x10/1/2020 01:00:00, …, x10/1/2020 23:00:00,
      x10/1/2021 00:00:00, x10/1/2021 01:00:00, …, x10/1/2021 23:00:00,
      …,
      x10/1/2029 00:00:00, x10/1/2029 01:00:00, …, x10/1/2029 23:00:00 )

## Slide 43: Topology Split in 3 parts

## Slide 46: Plant by Plant Presentations and Notes
Structured Exploration
Order – where did we start, where did we end up
  Classic* versus Historical (link)
  Classic* versus New (link)
  New versus Historical (link)
Description of
  Spreadsheet (monthly)
  (2) Envelope graphs (daily/hourly)
Free-Form Exploration
  Observations from previous conversations
  Questions from stakeholders
    Go into GENESYS live (if necessary) – hourly simulated data
    Go into the Army Corp site live (if necessary) – hourly historical data
  *Classic GENESYS has HYDSIM as a module, sometimes the results are referred to interchangeably
Not reviewed yet
Review Started But Incomplete
Review Completed

## Slide 47: Mica
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill– average and range

## Slide 48: Mica Scenario A

## Slide 49: Mica Scenario C

## Slide 50: Mica Scenario G

## Slide 51: Questions/Notes on Mica
Notes:
Investigate whether storage versus elevation table needs more data points (or different datapoints) to improve efficiency curves translation of net head to energy
  Why is the elevation higher in the classic model versus new model?

## Slide 52: Revelstoke
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill– average and range

## Slide 53: Revelstoke Scenario A

## Slide 54: Revelstoke Scenario C

## Slide 55: Revelstoke Scenario G

## Slide 56: Questions/Notes on Revelstoke
Notes:
BPA notes daily flexibility at Revelstoke (operating within a meter and a half for normal operating range)
Unlikely that Revelstoke could voluntarily drawdown without spilling
Further investigation on the Mica – Revelstoke coordinated operation should be conducted

## Slide 57: Arrow
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill– average and range

## Slide 58: Arrow Scenario A

## Slide 59: Arrow Scenario C

## Slide 60: Arrow Scenario G

## Slide 61: Questions/Notes on Arrow
Notes:
Why is the generation in the fall and the summer so much higher in the classic GENESYS? Investigate maximum turbine flow in classic.
  No discharge rate in classic GENESYS?
  H/k table difference?

## Slide 62: Duncan
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill– average and range

## Slide 63: Duncan Scenario A

## Slide 64: Duncan Scenario C

## Slide 65: Duncan Scenario G

## Slide 66: Questions/Notes on Duncan
Notes:

## Slide 67: Libby
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill– average and range

## Slide 68: Libby Scenario A

## Slide 69: Libby Scenario C

## Slide 70: Libby Scenario G

## Slide 71: Questions/Notes on Libby
Notes:
Why is Libby spilling in the overnight morning in the winter? Is this the max generation for the net head?
  Looks like Libby is at hydraulic capacity (i.e. max turbine flow) and thus any spill is actually probably disadvantageous for Libby itself. Probably this behavior for downstream concerns.

## Slide 72: Bonner’s Ferry
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill– average and range

## Slide 73: Bonners Ferry Scenario A

## Slide 74: Bonners Ferry Scenario C

## Slide 75: Bonners Ferry Scenario G

## Slide 76: Questions/Notes on Bonner’s Ferry
Notes:
Gauging station, not a dam

## Slide 77: Cora Linn
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill– average and range

## Slide 78: Questions/Notes on Cora Linn
Notes:
At Cora Linn, a canal was built to divert water to the Canal hydro project, which has a higher production factor than Cora Linn and the river plants below Cora Linn (Upper Bonnington, Lower Bonnington, South Slocan). A minimum flow of 5 kcfs is kept going through Cora Linn and the river plants, but water above this goes through Canal, up to full gate flow. Flows above full gate go through the river projects. The flows through Canal meet back up with the river flows at Brilliant.
Unfortunately, the new Genesys as currently configured cannot currently handle splitting the turbine or spill outflows from a project between two downstream projects and then having the flows meet back up again. What it does allow is for the turbine flows to be directed separately from the spill flows. So, currently, the way we are modeling it is that the turbine flows at Cora Linn are directed down through the river projects and the spill flows are directed through the Canal project.
A developer of HYDRO6 (a precursor to HYDSIM) stated that the way to solve the hydro modeling of Cora Linn and Canal is with dynamite.

## Slide 79: Kootenay Canal
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill– average and range

## Slide 80: Questions/Notes on Kootenay Canal
Notes:
See previous notes on Cora Linn

## Slide 81: Upper Bonnington
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 82: Questions/Notes on Upper Bonnington
Notes
See previous notes on Cora Linn

## Slide 83: Lower Bonnington
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 84: Questions/Notes on Lower Bonnington
Notes:
See previous notes on Cora Linn

## Slide 85: South Slocan
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 86: Questions/Notes on South Slocan
Notes:
See previous notes on Cora Linn

## Slide 87: Brilliant
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 88: Questions/Notes on Brilliant
Notes:
Modeled as ROR in HydSim, modeled as storage in new model
Can Brilliant actually have this volatile an operation? Is the extra flexibility significant in changing overall adequacy results?

## Slide 89: Hungry Horse
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 90: Hungry Horse Scenario A

## Slide 91: Hungry Horse Scenario C

## Slide 92: Hungry Horse Scenario G

## Slide 93: Questions/Notes on Hungry Horse
Notes:
Why does generation seem to peak higher in historical than in redeveloped? Investigate H/K table compared to classic

## Slide 94: Columbia Falls
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 95: Questions/Notes on Columbia Falls
Notes:
Gauging station not a dam

## Slide 96: SE¿LIŠ KSANKA QLISPE¿ Dam (will be referred to as SKQ)
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 97: Questions/Notes on SE¿LIŠ KSANKA QLISPE¿ Dam (will be referred to as SKQ)
Note:
For reference, this was formerly called Kerr Dam before the change in ownership in 2015.
Sounds like there are flow limits seasonally (PNCA), need a public source

## Slide 98: Thompson Falls
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 99: Questions/Notes on Thompson Falls
Notes:

## Slide 100: Noxon
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 101: Noxon Scenario A

## Slide 102: Noxon Scenario C

## Slide 103: Noxon Scenario G

## Slide 104: Questions/Notes on Noxon
Notes:
More movement in redeveloped GENESYS than we would expect per operations. Investigate implementation of Noxon forebay elevation ramp limitation modeled as a discharge rate.
  Look at inflows, if they are highly variable than discharge rate limitation will not necessarily be as useful in limiting forebay elevation.
Investigate H/K table interpolation, maximum generation is lower than classic consistently

## Slide 105: Cabinet Gorge
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 106: Cabinet Gorge Scenario A

## Slide 107: Cabinet Gorge Scenario C

## Slide 108: Cabinet Gorge Scenario G

## Slide 109: Questions/Notes on Cabinet Gorge
Notes:
Modeled as ROR in HydSim, modeled as storage in new model
More movement in redeveloped GENESYS than we would expect per operations. Do we have the correct operative storage limits?

## Slide 110: Priest Lake
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 111: Questions/Notes on Priest Lake
Notes:

## Slide 112: Albeni Falls
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 113: Albeni Scenario A

## Slide 114: Albeni Scenario C

## Slide 115: Albeni Scenario G

## Slide 116: Questions/Notes on Albeni Falls
Notes:
Check Excel sheet data on total outflow
Investigate H/K table interpolation, maximum generation is lower than classic consistently

## Slide 117: Box Canyon
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 118: Box Canyon Scenario A

## Slide 119: Box Canyon Scenario C

## Slide 120: Box Canyon Scenario G

## Slide 121: Questions/Notes on Box Canyon
Notes:
Look into why generation lower in classic versus redeveloped in spring

## Slide 122: Boundary
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 123: Questions/Notes on Boundary
Notes:
Modeled as ROR in HydSim, modeled as storage in new model

## Slide 124: Seven Mile
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 125: Questions/Notes on Seven Mile
Notes:
Modeled as ROR in HydSim, modeled as storage in new model

## Slide 126: Waneta
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 127: Questions/Notes on Waneta
Notes:
Modeled as ROR in HydSim, modeled as storage in new model

## Slide 128: Couer D’Alene
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 129: Questions/Notes on Couer D’Alene
Notes:

## Slide 130: Post Falls
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 131: Questions/Notes on Post Falls
Notes:

## Slide 132: Upper Falls
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 133: Questions/Notes on Upper Falls
Notes:

## Slide 134: Monroe Street
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 135: Questions/Notes on Monroe Street
Notes:

## Slide 136: Nine Mile
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 137: Questions/Notes on Nine Mile
Notes:

## Slide 138: Long Lake
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 139: Questions/Notes on Long Lake
Notes:
Use of H/K table may get slightly better results but under 10 MW difference.

## Slide 140: Questions/Notes on Little Falls
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range
Notes:
Modeled as ROR in HydSim, modeled as storage in new model

## Slide 141: Questions/Notes on Little Falls
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range
Notes:
Modeled as ROR in HydSim, modeled as storage in new model

## Slide 142: Grand Coulee
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill– average and range

## Slide 143: Grand Coulee Scenario A

## Slide 144: Grand Coulee Scenario C

## Slide 145: Grand Coulee Scenario G

## Slide 146: Questions/Notes on Grand Coulee
Notes:
Check minimum flow constraints at downstream projects in low water years to see how it effects operations.

## Slide 147: Chief Joseph
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 148: Chief Joseph Scenario A

## Slide 149: Chief Joseph Scenario C

## Slide 150: Chief Joseph Scenario G

## Slide 151: Questions/Notes on Chief Joseph
Notes:
Chief Joseph has wider operating range than in historical operations. Investigate whether updated operating ranges on Lower Snake and Columbia plants effects operating range on Chief Joe before changing constraints.
Check max pool and full pool at Chief Joseph
  Mismatch between HydSim range and historical operation

## Slide 152: Wells
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 153: Wells Scenario A

## Slide 154: Wells Scenario C

## Slide 155: Wells Scenario G

## Slide 156: Questions/Notes on Wells
Notes:
Traditionally, been operated at a higher head to prioritize generation
Look at using/developing a more detailed H/K table to better capture encroachment

## Slide 157: Chelan
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 158: Questions/Notes on Chelan
Notes:

## Slide 159: Rocky Reach
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 160: Rocky Reach Scenario A

## Slide 161: Rocky Reach Scenario C

## Slide 162: Rocky Reach Scenario G

## Slide 163: Questions/Notes on Rocky Reach
Notes:
Look at using/developing a more detailed H/K table to better capture effects of different head
Operating within full range of the plant’s storage may not allow for inflow uncertainty. Explore adding uncertainty or operating in a tighter pool without penalty and a broader pool with some penalty.
Research or get any further necessary max and total volume spill limitations that adhere to total dissolved gas limits

## Slide 164: Rock Island
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 165: Rock Island Scenario A

## Slide 166: Rock Island Scenario C

## Slide 167: Rock Island Scenario G

## Slide 168: Questions/Notes on Rock Island
Notes:
Look at using/developing a more detailed H/K table to better capture effects of different head
Operating within full range of the plant’s storage may not allow for inflow uncertainty. Explore adding uncertainty or operating in a tighter pool without penalty and a broader pool with some penalty.
Research or get any further necessary max and total volume spill limitations that adhere to total dissolved gas limits

## Slide 169: Wanapum
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 170: Wanapam Scenario A

## Slide 171: Wanapam Scenario C

## Slide 172: Wanapam Scenario G

## Slide 173: Questions/Notes on Wanapum
Notes:
Look at using/developing a more detailed H/K table to better capture effects of different head
Operating within full range of the plant’s storage may not allow for inflow uncertainty. Explore adding uncertainty or operating in a tighter pool without penalty and a broader pool with some penalty.
Research or get any further necessary max and total volume spill limitations that adhere to total dissolved gas limits
Maximum generation is a little low (follow-up with GCPUD)
Follow up with GCPUD about seasonal reductions in turbined flow (hydraulic capacity)

## Slide 174: Priest Rapids
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 175: Priest Rapid Scenario A

## Slide 176: Priest Rapid Scenario C

## Slide 177: Priest Rapid Scenario G

## Slide 178: Questions/Notes on Priest Rapids
Notes:
Increase priority of constraint and modify modeling to better enforce minimum outflows
Look at using/developing a more detailed H/K table to better capture effects of different head
Operating within full range of the plant’s storage may not allow for inflow uncertainty. Explore adding uncertainty or operating in a tighter pool without penalty and a broader pool with some penalty.
Research or get any further necessary max and total volume spill limitations that adhere to total dissolved gas limits
October and November maximum discharge limit during daytime
Stranding bands and TDG% issues seem to be mitigated by some of the minimum outflow constraints (follow-up with GCPUD)
  There may be to model this that has less upstream effects

## Slide 179: Brownlee
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 180: Brownlee Scenario A

## Slide 181: Brownlee Scenario C

## Slide 182: Brownlee Scenario G

## Slide 183: Questions/Notes on Brownlee
Notes:
Investigate whether storage versus elevation table needs more data points (or different datapoints) to improve efficiency curves translation of net head to energy
Total outflows are higher during some periods, is this an issue at the frequency that they occur in the model?

## Slide 184: Oxbow
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 185: Questions/Notes on Oxbow
Notes:
Modeled as ROR in HYDSIM, but has usable storage in redeveloped model
Investigate whether it is necessary to use an H/K table versus average H/K

## Slide 186: Hells Canyon
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 187: Hells Canyon Scenario A

## Slide 188: Hells Canyon Scenario C

## Slide 189: Hells Canyon Scenario G

## Slide 190: Questions/Notes on Hells Canyon
Notes:
Modeled as ROR in HYDSIM, but has usable storage in redeveloped model
Investigate whether it is necessary to use an H/K table versus average H/K
Investigate whether it uses all of usable storage or allow for buffer to account for inflow uncertainty

## Slide 191: Dworshak
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 192: Dworshak Scenario A

## Slide 193: Dworshak Scenario C

## Slide 194: Dworshak Scenario G

## Slide 195: Questions/Notes on Dworshak
Notes:
Investigate whether storage versus elevation table needs more data points (or different datapoints) to improve efficiency curves translation of net head to energy

## Slide 196: Lower Granite
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 197: Lower Granite Scenario A

## Slide 198: Lower Granite Scenario C

## Slide 199: Lower Granite Scenario G

## Slide 200: Questions/Notes on Lower Granite
Notes:
Operating ranges on Lower Granite in operations have different floor depending on flow into the plant. Explore modifying MOP range by floor (look at min flow constraint at Dworshak and modify floor on MOP)
See how any changes impact Little Goose
Follow-up to see how/if temperature limits are incorporated in the modeling. If not, see what we can do to approximate (follow with technical management team)

## Slide 201: Little Goose
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 202: Little Goose Scenario A

## Slide 203: Little Goose Scenario C

## Slide 204: Little Goose Scenario G

## Slide 205: Questions/Notes on Little Goose
Notes:
Check 2022 C Bypass spill constraints

## Slide 206: Lower Monumental
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 207: Lower Monumental Scenario A

## Slide 208: Lower Monumental Scenario C

## Slide 209: Lower Monumental Scenario G

## Slide 210: Questions/Notes on Lower Monumental
Notes:

## Slide 211: Ice Harbor
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 212: Ice Harbor Scenario A

## Slide 213: Ice Harbor Scenario C

## Slide 214: Ice Harbor Scenario G

## Slide 215: Questions/Notes on Ice Harbor
Notes:

## Slide 216: McNary
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 217: McNary Scenario A

## Slide 218: McNary Scenario C

## Slide 219: McNary Scenario G

## Slide 220: Questions/Notes on McNary
Notes:
No target storages used, only seasonal operating pool constraints
Per observed elevations, remove MOP constraints in the summer align with normal operating range year round

## Slide 221: John Day
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 222: John Day Scenario A

## Slide 223: John Day Scenario C

## Slide 224: John Day Scenario G

## Slide 225: Questions/Notes on John Day
Notes:
No target storages used, only seasonal operating pool constraints
Per observed elevations, retain MOP constraints in the summer align with normal operating range year round
Check H/K table interpolation

## Slide 226: Round Butte
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 227: Questions/Notes on Round Butte
Notes:
Fish collection facility means they have limited elevation range they can operate in.

## Slide 228: Pelton
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 229: Questions/Notes on Pelton
Notes:

## Slide 230: Reregulating Dam
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 231: Questions/Notes on Reregulating Dam
Notes:

## Slide 232: The Dalles
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 233: The Dalles Scenario A

## Slide 234: The Dalles Scenario C

## Slide 235: The Dalles Scenario G

## Slide 236: Questions/Notes on The Dalles
Notes:
No target storages used, only seasonal operating pool constraints
Per observed elevations, remove MOP constraints in the summer align with normal operating range year round

## Slide 237: Bonneville
  Outflow – average and range
  Generation – average and range
  Ending elevation – average and range
  Spill – average and range

## Slide 238: Bonneville Scenario A

## Slide 239: Bonneville Scenario C

## Slide 240: Bonneville Scenario G

## Slide 241: Questions/Notes on Bonneville
Notes:
No target storages used, only seasonal operating pool constraints
Per observed elevations, remove MOP constraints in the summer align with normal operating range year round
Increase priority of constraint and modify modeling to better enforce minimum outflows

## Slide 242: System Flexibility and Market
Market risk and structure, transmission

## Slide 243: Placeholder for System Flexibility and Market Info
Review of Model Stages
Market and transmission utilization
Hourly hydro flexibility
Market interactions on thermal unit commitment
  Low thermal commitment
Role of reserves
This Photo by Unknown Author is licensed under CC BY-NC

## Slide 244: Example: How Does Redeveloped GENESYS Simulate Hourly Operation?
October
Commit for Monday, Plan for Tuesday through Sunday
Account for energy, reserves, and for fuel usage in Hour 1
Commit for Hour 2, Plan for Hours 2 through 24 and Hour 1 of next day.
Commit for Tuesday, Wednesday through Sunday.
Weekly Forecast
Day-Ahead Commitment
Hour-Ahead Commitment
Deployment (True-Up)
...
Commit for Hour 24, Plan for Hours 1 through 23 of next day
Account for energy, reserves, and for fuel usage in Hour 2.
…
Account for energy, reserves, and for fuel usage in Hour 24.
Commit for Hour 1, Plan for Hours 2 through 24
Accounting
Cost Optimization
Notes: This is an example for October.

## Slide 245: Expanded External Market Modeling Capability
More detailed transmission topology
Each “bubble” represents a balancing authority, multiple balancing authorities or part of a balancing authority depending on transmission constraints.
Hourly loads for each bubble.
Resources in each bubble represented by bins of the amount of market resource available at a price (hourly) OR as a individually modeled resource.
Currently, most of the resources in the region are represented as individual resources and most external to the region are represented as bins of market resource.

## Slide 246: 18.4% More Useable Storage in US in Redeveloped GENESYS
Units of Useable Storage | Classic GENESYS | Redeveloped GENESYS
Net (KSFD) | 13,132 | 15,553
Net (MAF) | 26.0 | 30.8
Plants with reservoirs in new model and modeled as run-of river in HYDSIM and classic GENESYS:
Alder
Boundary
Cabinet Gorge
Diablo
Gorge
Hells Canyon
Mayfield
Oxbow
Pelton
Priest Rapids
Rock Island
Rocky Reach
Wanapum
Wells

## Slide 247
Chart: Average Lower Columbia Hydro Generation Range
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Simulated | 1428.3074 | 1458.4122 | 1342.593 | 910.4841 | 1080.4905 | 1086.3202 | 802.7321 | 641.7133 | 774.8949 | 768.1636 | 1260.6236 | 1280.9003
Historical Ten Years | 1247.4751 | 1025.9719 | 1025.8921 | 755.8557 | 745.9906 | 712.5671 | 861.8932 | 754.0916 | 978.5355 | 973.6271 | 1167.1554 | 1255.596
Chart: Average Daily Generation Range By Month for Lower Columbia Plants Historical versus Simulated
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
2010 | 1107.2684 | 944.5454 | 1069.7206 | 749.9103 | 1020.1884 | 774.8107 | 946.9771 | 444.5655 | 776.4757 | 1016.0613 | 1409.0848 | 1786.4313
2011 | 1492.1558 | 1208.1104 | 1348.4858 | 672.2287 | 649.4552 | 323.169 | 819.8913 | 1260.26 | 1402.5867 | 1266.8452 | 1340.663 | 1466.8048
2012 | 1591.539 | 1371.5579 | 1052.21 | 725.709 | 626.7229 | 802.469 | 1081.8881 | 1425.8729 | 1198.0993 | 887.8148 | 1349.4148 | 1254.9229
2013 | 1517.6023 | 1414.7854 | 1400.4726 | 808.6097 | 664.8239 | 885.8533 | 1009.45 | 942.6123 | 987.7707 | 1057.9158 | 1243.802 | 1351.8506
2014 | 1445.3635 | 1390.1271 | 869.9687 | 771.3453 | 682.2503 | 745.0573 | 1037.7284 | 868.9419 | 845.1687 | 850.8803 | 1169.4347 | 1120.8265
2015 | 1065.98 | 824.1525 | 1187.2545 | 774.9253 | 689.8994 | 553.3843 | 501.7797 | 525.9877 | 897.1823 | 832.2842 | 940.606 | 1341.4103
2016 | 1263.9845 | 1199.8352 | 1105.8294 | 595.4663 | 667.221 | 823.74 | 755.4739 | 522.3497 | 946.598 | 967.2245 | 968.6953 | 1126.2452
2017 | 1152.3839 | 545.7867 | 391.6252 | 259.9577 | 311.9303 | 395.8467 | 862.4952 | 537.7606 | 964.4223 | 872.23 | 1166.8663 | 1175.3107
2018 | 779.9897 | 332.4032 | 428.1774 | 861.4683 | 398.7474 | 692.0263 | 1073.7006 | 533.2529 | 941.1207 | 877.6797 | 1391.8302 | 1127.0332
2019 | 1158.9058 | 1108.0696 | 1107.8058 | 1231.666 | 1275.209 | 972.058 | 571.3616 | 435.7465 | 822.0887 | 993.5987 | 914.319 | 1059.6271
2020 | 1147.0529 | 946.3176 | 1323.2632 | 863.1257 | 1219.4484 | 869.8237 | 820.079 | 797.6574 | 982.377 | 1087.3632 | 943.9927 | 1001.093
1 | 1146.3194 | 1384.7491 | 1206.9887 | 768.2941 | 829.2492 | 998.3789 | 727.8149 | 523.9514 | 831.6264 | 1084.2012 | 1425.0201 | 1132.3252

## Slide 248
Chart: Average Daily Generation Range By Month for Mid-C Plants Historical versus Simulated
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Simulated | 1538.0947 | 1584.5343 | 2048.8104 | 2193.7242 | 2018.9539 | 1791.067 | 2380.9629 | 2590.7684 | 2463.9992 | 2202.85 | 2231.2757 | 1807.3205
Historical 2010-2020 | 1180.7537 | 1244.546 | 1042.9243 | 963.1706 | 612.7903 | 716.0997 | 1071.9557 | 1212.1132 | 1418.3621 | 1453.8252 | 1543.373 | 1308.3433
Chart: Average Daily Generation Range By Month for Mid-C Plants Historical versus Simulated
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
2010 | 1832.2677 | 1775.8357 | 1454.183 | 1289.6533 | 1266.9387 | 873.54 | 1522.2484 | 2248.1032 | 1467.4167 | 1738.7484 | 1844.9912 | 1733.0194
2011 | 1138.1387 | 714.8714 | 897.8097 | 718.8933 | 469.4935 | 562.67 | 1872.7806 | 1019.8194 | 1861.3467 | 1701.371 | 1919.3428 | 1690.3129
2012 | 1414.3 | 1813.1241 | 1070.3806 | 663.0767 | 438.2581 | 576.29 | 578.3387 | 662.0161 | 1848.13 | 1700.3581 | 2015.7718 | 1142.7452
2013 | 799.4903 | 1468.3357 | 1424.9871 | 600.82 | 536.8645 | 550.42 | 725.4613 | 1408.2387 | 1681.63 | 1564.1935 | 1330.1933 | 1175.7742
2014 | 1370.5032 | 1483.5786 | 940.6742 | 603.9867 | 358.1871 | 513.0233 | 763.4613 | 1016.0065 | 1170.23 | 1207.6839 | 1047.27 | 1218.2839
2015 | 832.2548 | 551.95 | 664.2323 | 1025.9033 | 1171.2581 | 1411.53 | 1404.6968 | 1363.7129 | 1309.72 | 1327.0129 | 1699.9433 | 1566.5065
2016 | 1372.6742 | 1293.3586 | 851.0355 | 2116.3767 | 680.5935 | 853.8233 | 1129.7065 | 1087.7419 | 1347.4967 | 1418.6774 | 1143.1133 | 800.4355
2017 | 585.9516 | 836.8233 | 694.7032 | 558.6633 | 364.7032 | 426.9633 | 937.2516 | 1235.5645 | 1285.22 | 1338.0903 | 1511.5 | 1436.1647
2018 | 783.4065 | 395.3429 | 846.8935 | 621.9067 | 324.4968 | 543.61 | 1040.8516 | 1318.6774 | 1429.1667 | 1537.3258 | 1389.4034 | 1636.2258
2019 | 1641.6548 | 1984.8786 | 1456.5871 | 1301.0867 | 655.4871 | 1044.79 | 1340.7613 | 1180.1226 | 1166.1633 | 1252.4581 | 2175.6467 | 1060.5387
2020 | 1217.6484 | 1371.9069 | 1170.6806 | 1094.51 | 474.4129 | 520.4367 | 475.9548 | 793.2419 | 1035.4633 | 1206.1581 | 899.9267 | 931.77
1 | 1559.7649 | 1744.6824 | 2113.5128 | 1638.753 | 1890.4924 | 1492.9354 | 2769.5717 | 2672.6329 | 2142.602 | 2334.446 | 1889.0088 | 1677.6241
Mid-Columbia plants operated as run-of-river in HydSim (i.e. no daily flexibility)

## Slide 249: Next Steps on Hydro Operations
Changes between Draft and Final, changes after the plan…

## Slide 250: General Notes/Requests
Show a graph that compares monthly average imports between the new and the classic
Interest in a scenario where a transmission line is taken out for month or so (proxy for wildfire) and what the implications are for adequacy?
  COI or PDCI or something internal?

## Slide 251: Since Initial Stakeholder Comments
Major changes:
  Imposed maximum spill limits on most plants to not be violated for economic purposes
    Based on physical limits in most cases and operations where available
  Modified penalties on some plant constraints
  PSR fixed model to override inconsistencies between hourly discharge rate penalties and target storage to ensure water balance
  Tightened target storage tolerance on Mica and Dworshak
  Increased Mica useable storage to better align with HYDSIM per hydro experts
  Moved from average H/K to H/K tables for many reservoirs.

## Slide 252: Next Steps
Incorporate stakeholder feedback, if and as possible
Investigate whether storage versus elevation table needs more data points (or different datapoints)
Update MOP constraints on Lower Granite to estimate the variable flow floor modifying MOP range (look at min flow constraint at Dworshak and modify floor on MOP)
Remove MOP constraints on McNary, The Dalles, Bonneville, return to normal operating range year round
Check MOP effective date ranges per the Biological Assessment (some dates seem slightly off)
Return to normal operating storage on John Day when MOP not in effect
Investigate whether updated MOP on above plants effects operating range on Chief Joe
Increase priority of constraint and modify modeling to better enforce min outflows at Priest rapids and Bonneville
Investigate implementation of Noxon forebay elevation ramp limitation modeled as a discharge rate (more movement in redeveloped GENESYS than we would expect)

## Slide 253: Comparisons between GENESYS and Historical Data
August 4 – 6, 2021

## Slide 254: Extras

## Slide 255: Chief Joseph

## Slide 256: Rock Island